## Slide 1: Iot Based Cow Health Monitoring System
Under the Guidance of
Dr Aravinda Thejas Chandra
Professor
Department of information science and engineering
SJC Institute of Technology
Project Work Phase – 1: Review - 2
Presented By
Ganavi S 1SJ22IS036
Kruthika S 1SJ22IS053
Likhitha N 1SJ22IS056
Bhavana M 1SJ22IS017

## Slide 2
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 1
Contents
  Objectives
  Methodology
  Plan of execution

## Slide 3
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 2
Objectives
To design and develop the cow health lump detection system using iot and image processing
To detect the cow fever using temperature sensor
To detect the watering eye and mouth using moisture sensor
To alert the former using buzzer
To update the status to doctor and former mobile app using wi-fi

## Slide 4
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 3
Methodology
1. Requirement Analysis
The initial phase involves identifying the key health parameters necessary for effective monitoring of cattle. Common parameters include:
Body temperature
Heart rate
Physical activity
Ambient conditions (temperature and humidity)
GPS location
Input from veterinarians and livestock farmers is gathered to finalize the critical metrics.

## Slide 5
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 3
2. Sensor Selection and Integration
Appropriate sensors are selected and integrated into a wearable or non-invasive device. These may include:
Temperature sensor (e.g., DS18B20)
Heart rate sensor (e.g., pulse sensor or ECG module)
Accelerometer (e.g., MPU6050) for activity tracking
GPS module (e.g., Neo-6M) for tracking location
DHT11/DHT22 for ambient temperature and humidity
These sensors are connected to a microcontroller ( Arduino UNO) capable of processing data and supporting wireless communication.

## Slide 6
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 4
3. Data Acquisition and Transmission
Sensor data is continuously collected and transmitted to a central cloud server using wireless communication protocols such as:
Wi-Fi (if within range)
LoRa (for long-range, low-power environments)
GSM/GPRS (for remote locations without Wi-Fi)
4. Cloud Storage and Processing
A cloud platform (e.g., Firebase, ThingSpeak, AWS IoT Core) receives and stores data in real-time. Processing includes:
Filtering and validation of sensor data
Statistical analysis for trend monitoring
Alert generation for abnormal readings

## Slide 7
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 5
5. Data Analysis and Alert System
An intelligent algorithm (rule-based or machine learning) analyzes historical data to detect anomalies like:
Elevated body temperature (fever)
Low activity levels (signs of illness)
Abnormal heart rate
When abnormal values are detected, alerts are sent to the farmer or vet via SMS, mobile app notifications, or email.
6. User Interface Development
A mobile or web-based dashboard is developed to allow users to:
View real-time health metrics
Track historical trends

## Slide 8
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 6
Receive alerts and recommendations
Tools such as Flutter, React Native, or Android Studio can be used for mobile apps, while HTML/CSS/JS or frameworks like React can serve for web interfaces.
7. Testing and Evaluation
The prototype is tested on a small number of cows over a period to assess:
Sensor accuracy and reliability
Data transmission success rate
Timeliness and relevance of alerts
User interface usability
Feedback from veterinarians and farmers is used to iterate and improve the system.

## Slide 9
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 6
8. Outcome
Real-time cow health monitoring
Early detection of diseases
Easy access for farmers via app or web

## Slide 10
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 6
MICRO CONTROLER
POWER SUPPLY
LCD DISPLAY
TEMPERATURE SENSOR
BUZZER
MOISTURE SENSOR
UART
WI-FI
Mobile APP
PC WITH MATLAB
BLOCK DIAGRAM

## Slide 11
Iot Based Cow Health Monitoring System Group -30
Dept. of ISE,SJCIT 2025 6
Activities | OCT 15 | NOV 10 | DEC 10 | JAN 10 | FEB 08 | MAR 15 | APR 3 | APR 25 | MAY 10-20
Planning phase |  |  |  |  |  |  |  |  | 
Literature survey |  |  |  |  |  |  |  |  | 
Analysis phase |  |  |  |  |  |  |  |  | 
Desingn phase |  |  |  |  |  |  |  |  | 
Implentation |  |  |  |  |  |  |  |  | 
Testing |  |  |  |  |  |  |  |  | 
Deployment |  |  |  |  |  |  |  |  | 
Document report |  |  |  |  |  |  |  |  | 
PLAN OF EXECUTION

## Slide 12
THANK YOU